## Slide 1: FAULT SIMULATION
Dr. Gaganpreet Kaur

## Slide 2: Problem
Given
    A circuit
    A sequence of test vectors
    A fault model
Determine
    Fault coverage - fraction (or percentage) of modeled faults detected by test vectors
    Set of undetected faults
Motivation
    Determine test quality and in turn product quality
    Find undetected fault targets to

## Slide 3: Fault Simulation in VLSI

## Slide 4: Fault Simulator
A fault simulator is like an ordinary simulator, but needs to simulate two versions of a circuit
(i) without any fault for a given input pattern and
(ii) with a fault inserted in the circuit and for the same input pattern.
The outputs under normal and faulty situation are compared and if they differ, the pattern detects the fault.
•Step (ii) is repeated for all faults.

## Slide 6: Fault Simulation
The procedure is simple, but is too complex in terms of time required.
While the multiple detection of a fault, is desirable for fault it is expensive in computation time.
Solution: fault dropping,
considerably speeds up the fault simulation process.

## Slide 7: Serial Fault Simulation
First, Simulate fault-free circuit and save responses.
Repeat following steps for each fault in the fault list:
    Modify netlist by injecting one fault
    Simulate modified netlist, vector by vector, comparing responses with saved responses
    If response differs, report fault detection and suspend simulation of remaining vectors
Advantages:
    Easy to implement; needs only a true-value simulator, less memory
    Most faults, including analog faults, can be simulated

## Slide 8
Consider Inputs A=1, B=1

## Slide 9: Parallel simulation
Exploits inherent bit-parallelism of logic operations on computer words
Storage: one word per line for two-state simulation
Multi-pass simulation: Each pass simulates w-1 new faults, where w is the machine word length
Speed up over serial method ~ w-1
Not suitable for circuits with timing-critical and non-Boolean logic

## Slide 11: Deductive fault simulation
One-pass simulation
Each line k contains a list Lk of faults detectable on it
fault lists of all gate output lines are updated using set-theoretic rules, signal values, and gate input fault lists
PO fault lists provide detection data
Limitations:
    Set-theoretic rules difficult to derive for non-Boolean gates
    Gate delays are difficult to use

## Slide 15: Concurrent fault Simulation
Event-driven simulation
only those components/gates of the faulty circuit simulated that differ in signal states from the fault-free circuit.
A list per gate maintained
List element contains fault ID, gate input and output values and internal states, if any.
Retains list when moving from one pattern to another.
Faster than other methods, but uses most memory.